## Slide 1: Computer modeling of laser propagation and beam control through atmospheric turbulence: A WaveTrain Tutorial
Captain Matthew R. Whiteley, Ph.D.
Airborne Laser Technologies Branch
AFRL/DEBA
Directed Energy Directorate
Air Force Research Laboratory

## Slide 2: “Wave-Optics” Simulation
“Simulation” can mean many things:
  Anything designed to look or act like something else
  Computer processing using synthetic signals: random processes—inject signal with correct PSD
  Modeling of a physical process—based on first-principles, physical laws, key assumptions
“Wave-Optics”
  Treating propagation light with full wave properties
  Spatial evolution given by Fresnel approximation
  Turbulence: Kolmogorov phase screens, “Markov” model—uncorrelated phase induced at discrete locations

## Slide 3: Why Simulation?
Nature of propagation through random media
  Propagation theory not (yet) fully developed
    “Rytov approximation” only valid for weak scattering
    Path integral expressions complicated, do not provide general solution to wave equation
  Wave-optics simulation is a technique for solving wave equation even in strong turbulence
Complex system modeling
  Theory developed using simplifying assumptions—may not be valid for system being studied
  Enhanced fidelity: Control systems, sensor effects, radiometry
  System architecture: target illumination, local-loop control

## Slide 4: Simulation using Phase Screens
Each screen is produced independently using method previously described.
Array size must be carefully chosen to account for diffraction effects.
Taylor’s frozen flow can be used to incorporate time effects.
Repeat for each screen

## Slide 5: What is WaveTrain?
Multi-user platform for wave-optics simulation
  Most WOCs are single-user, “fixed” code set
  Provides toolset for system assembly—use GUI to construct C++ code
  Object-oriented code permits modularity, hierarchy
  Systems::WaveTrain as mfiles::Matlab
Development history
  Builds on existing WOCs—ACS, MOLLY, YAPs, tOSC
  Funded by AFRL/DE SBIR—MZA Associates
  Model development supported by individual programs
  Emerging commercial user base: everything from eye surgery to HEL resonator design (AO fits in there somewhere!)

## Slide 6
Propagation Model: NOP-Salinas Peak
0.75 m aperture telescope, 50 km path
1 micron wavelength
2xCLEAR-1 atmosphere
10 m/s uniform wind
1000 Hz frame rate, 0.2 sec interval
camera image
of point source
Incident pupil
intensity
image of target
Intensity
0.50 m diameter
circle overlay
pupil
phase

## Slide 8: ABL SPO IVV&A Model
WaveTrain ABL model will be the government code for assessing PDRR system tests & for beam control technology transition

## Slide 9: Systems & Runsets
WaveTrain Systems (what the sim does)
  Defines components included a simulation
  Defines flow of light and signals through simulation
  Identifies inputs, outputs, and parameters
WaveTrain Runsets (how the sim does it)
  Built using WaveTrain system—many runsets, one system
  Specify value of system parameters
  Define run variables—parameters may depend on run variables

## Slide 10: Tutorial Schedule
System Name
System Description
Principles
TutA.tsd
Vacuum propagation of laser from optical system to target board
WaveTrain user interface; building runset; data loading & analysis
WindAtmoPath.tsd
Add transverse velocity to atmospheric path, create subsystem
System inputs & outputs; creating/using WaveTrain subsystems
TutB.tsd
Add atmospheric path for propagation; Add point source & imaging camera
Random turbulence realizations; Temporal turbulence effects; Beam projection vs. imaging
TutC.tsd
Add beam steering mirror
Coordinate systems; pointing control
TutD.tsd
Add centroid processing
Camera processing in simulation environment

## Slide 11: Tutorial Schedule (cont.)
System Name
System Description
Principles
TutE.tsd
Close the track loop
Closed-loop beam steering/control
TutF.tsd
Add incoherent extended target with target-end illumination; Add point source scoring sensor, target board processing
Speckle averaging methods; Reflectance maps; Tracking from extended sources
TutG.tsd
Add illuminator at system transmitter
Active illumination of target; incoherent target return; Beam reciprocity & tilt indetermination
TutH.tsd
Return to point source reference, add higher-order wave-front sensor
WFS inputs & reconstructor outputs; Hartmann sensor imagery, slopes
TutI.tsd
Closed-loop higher-order control
Higher-order beam compensation—fixed and random aberrations

## Slide 12: Tutorial System A “TutA”

## Slide 13: Subsystem “WindAtmoPath”

## Slide 14: Tutorial System B “TutB”

## Slide 15: Tutorial System C “TutC”

## Slide 16: Tutorial System D “TutD”

## Slide 17: Tutorial System E “TutE”

## Slide 18: Tutorial System F “TutF”

## Slide 19: Tutorial System G “TutG”

## Slide 20: Subsystem “WFSandRecon”

## Slide 21: Tutorial System H “TutH”

## Slide 22: Tutorial System I “TutI”